- broadly, the system is divided into core and non-core
  components
        - according to the underlying OS and
        hw architectures, certain design and
        implementation details may vary
        - in any system, core and non-core will
        be present - just they way they are
        managed will be different
- they are further resident in two different spaces -
  user-space / system -space
     - in such design and implementations, there will
       be an effective separation of user-space and
       system-space memory regions - this is denoted,
       by a dotted-line - this isolation/separation/
       protection is done, with the help if hw features
       and OS management - low-level features of
       hw and OS are used

-- Architecture --> design --> implementations --> ???

- user-space is set-up, using address-space of processes -
  this is done, with the help of hw attributes of the
  processor, along with hw memory management techniques
 - some of these details will be explored, in
   memory management
note: we will be studying more on processes, soon ???
note: we will study and understand address-spaces/logical
      - address-spaces and virtual address-spaces
- system-space is also set-up, using address-space of
  processes - this is also done, with the help of
  hw attributes and hw memory management techniques -
  more, during memory management
- more discussions, during process address-space
- in OS platforms, there are different sets of
  memory-maps, different from conventional embedded ??
- address-space is popular, in OS platforms
- memory-map is popular, in conventional embedded

- refer to the diagrams, in linux_slides_1.pdf - this
  diagram will be explored, during memory management

- core components are typically resident, in kernel-space
  and the arch. of the kernel /core of OS is monolithic
  - meaning, all the core components/modules are linked
  together to form a single kernel image, which is
  loaded, during the boot-up time - the kernel image
  /monolithic image contains static modules, not
  dynamic modules
    - as per OS platform, following are typical core
      components :
        - process subsystem/manager
        - thread subsystem/manager
        - cpu scheduling subsystem/manager
        - IPCS mechanisms/sub-systems
        - IO subsystems
        - device driver modules
        - ......
note: in the context of core of the operating system,
      components are typically implemented, as static
      or dynamic modules
note: in conventional embedded platforms/stacks,
      static modules are very popular
- for practical convenience/flexibility, dynamic
  modules, which will be loaded / unloaded, as needed
- in a typical GPOS system, static and dynamic modules
  are popular
- in an RTOS/EOS system, static may be more popular,
  than dynamic modules
note : in this document, Linux is used, as the
       OS/GPOS platform
- the typical kernel images are present under /boot
  directory

- whereas, dynamic modules are typically present, in
  the /lib/modules/<kernel-version>/* directories

- depending upon the kernel configuration/set-up,
  certain modules will be added as static modules
  and certain modules will be added, as dynamic modules

- refer to the kernel configuration details of the
  Vendor's kernel - you may need to update/upgrade the
  kernel images/modules, as needed ???
- it is common to reconfigure/rebuild GPOS/EOS/RTOS
  platforms, as per project's/application's requirements
- in the case RTOS, before starting the project, we
  must finalize the configuration settings and
  do a rebuild of the image / RTOS system

- kernel image / dynamic modules reside, in the kernel
  space/system space, after loading

note:in the case of GPOS, the above set-up is a common
     architecture and design
note:in the case of EOS/RTOS, the above set-up is one
     of the arch./designs, but there are other possible
     architectures/designs ???
note: initially, we will accept and assume, that
      the OS archicture and design will be
      monolithic and user-space/system-space

- typical kernel components/modules are passive
  entities, in the kernel space/system-space -
  meaning, they are loaded and resident
  passively - there are certain exceptions to
  this rule - we will see, as needed ???

- typically, core components will execute
  , during system booting, for initialization
  - once initialization is done, they are
  resident, as passive entities “Passive means they do nothing”

- what is the meaning of passive entities ???
    - passive, in this context means, they are
      not processes/threads/kernel threads - they
      are just modules, which are loaded and resident,
      in the system ?? since these are passive
      entities, they will not be scheduled,
      explicitly - if they are not explicitly
      scheduled, how are they executed / processed ???
      - these components are event triggered - these
     events are hw interrupts and their processing,
     system call APIs and their processing, and
     processor fault exceptions and their processing ??
     - the processing is done, as part of some
     event processing - these are some of the
     true characteristics of a monolithic kernel
    - in these discussions, let us assume, that
      there is an active application/process
      currently executing, in the system
    - while this active application/process
      is executing,what happens, if there is a
      hw interrupt event ??
    - what are the actions taken, by the hw and
      operating system ???

    - refer to lecture diagrams on hw int. events
      and system call APIs ??? understand
      , how these events are processed, in an
      OS platform ???
       - there are several hw actions and
        OS actions - we will see more details
        , in the upcoming sessions ???
       - in these contexts, as part of
        ISR/handler processing, apart
        from regular processing, kernel
        components/modules/services will be
        invoked - that is the design and set-up
       - once the basic processing is done,
        as before, the process/active application
        is resumed
       - there are principles and rules, for writing
        OS-aware-ISRs ???
       - we will also understand the details, using
        appropriate scenarios ???
       - system call APIs and their services is
        commonly used, in OS platforms - this is
        how OS exports its services
       - in typical GPOS systems and sophisticated
        EOS/RTOS systems, system call APIs are
        entry to OS core services
       - system call APIs use special machine
        instructions, which generate interrupt
        events - these instructions are known,
        as low-level trap instructions - the basic
        principles of interrupts and system call
        APIs/machine instruction/trap are same,
        but implementation details are different
       - refer to the lecture diagrams on
        system call APIs and their internal working
        ???
       - in the case of a typical system call API,
        an interrupt like jump is executed and
        after the jump, there is a thorough processing
        ,using tables and system call service rountines -
        - for each system call API, a specific routine
        is processed and a system service is
        completed ???
note: for the above set-up/frame-works to work,
      low-level features of processor/hw and
      OS are used, which eventually, provides
      high-level services to user-space
      and applications

note: what is user-mode/less-privileged mode ??
      in this processor mode,the privileges
      are restricted, like limited access
      to memory-map/address-space and
      hw resources
note: what is system-mode/privileged mode ??
      in this processor mode,the privileges
      are unrestricted access to memory-map/
      address-space and hw resources
note: these manipulations of modes are done,
      by kernel of the OS, as per architecture
      and design ???
note: what is the practical impact of these
      modes on operating system components and
      applications ???
      - core of the OS/kernel is provided
        unrestricted access to hw resources
        and memory-map/address-space
      - however, non-core components and applications
        are not provided direct access to the
        hw resources and memory-map
      - however, the non-core components and
        applications are provided access to
        hw resources and other services of
        kernel, using system call APIs ???
        - refer to the lecture diagram on
        system call API and switch, in
        processor privilege levels ??
        - after a system call API, there is a
        temporary mode switch to privileged mode
        and appropriate service routine is
        executed - once the service routine
        is completed, there will be return
        from the interrupt action and the
        mode will be again switched back to
        less privileged and execution
        resumes, in user-space ???
note: in the case of conventional embedded
      sw models, application code /program
      will have unrestricted access to
      entire memory-map and address-space
      - this may be acceptable, for simple
      embedded systems, but not critical
      embedded systems ??

- what is the meaning of active entities ???
    - active entities are managed, using processes/
      threads, explicitly - most core components
      are managed, as active entities, using
      processes/threads - it depends on the
      multitasking sw model used - based on the
      multitasking sw model, processes may used or
      threads may be used, or a hybrid multitasking
      of processes and threads will be used ??
note: initially, we will be dealing, with a simple
      multi-tasking model, using processes only
note: however, as per the OS platforms and application
      requirements, we may encounter different
      multitasking sw models, like hybrid and
      threads only ??

    - every system utility is managed, using
      a process, when loaded/launched - initially,
      when we use GPOS system, for our learning,
      we will execute several utilities, like
      system utilities, for regular operations -
     all these utilities are loaded and
     managed, as processes ???

    - in addition, there will be several system
      processes/daemons, which will be also
      loaded/launched and managed, as processes ??
      - in this case, you need to understand
      characteristics of special processes, like
      daemons ??

     - ideally, most modern GPOS systems, like
       Unix / Linux support multiprocessing -
       there is support, for multiple processors -
       the main support is provided, by the
       kernel / and its components - for instance,
       there is support, for multiprocessor
       scheduling, in addition to regular cpu
       scheduling - as part of this, several
       features are implemented, like load
       balancing of processes/threads among
       the processors, one set of RQs per
       processor, setting processor affinities/pinning,
       for processes, and many more
note: real-world systems are multi-processor systems
      and a sophisticated OS is needed to manage
      resources and applications
     - in a multiprocessor system, multitasking
       is supported, along with parallelism - this
       can support several processes/threads to
       simultaneously execute on different processors
note: we will be using multiprocessing, during our
      labs and assignments ???

     - most of these core services are exported to
       user-space and it is upto the high-level applications
       and services to exploit appropriate services ???
        - high-level services(can be non-core components
        of the OS/system services) may use a form
        of multitasking/multiprocessing
note : non-core components are system utilities + system
       libraries + system processes/services of
       a given OS
     - in addition, non-core components execute, as
       processes, with following characteristics:
        - the low-level cpu execution privilege
        is less-privileged-level

        - as a consequence, they have restricted
        access to resources / IO /kernel space

        - they are allowed to access core services
        /kernel space, using system call APIs, but
        there are very strict restrictions

        - many of these issues will be seen, when
        we use different system utilities and
        system call APIs

        - all non-core components are loaded and
        executed, in user-space of their
        respective processes and they do not
        have direct access to kernel-space of
        the system
note: in GPOS systems, most activities and features
      are built around processes/threads/files/memory
      management
note: in RTOS systems, most activities and features
      are built around threads/drivers/IO/strict
      memory management/sw timers

        - both applications' processes and system utilities/
        services, invoke system call APIs, for their
        requirements - whenever a system call API is
        invoked, there is a special jump to the kernel-
        space and in addition, there is a mode switch -
        meaning, cpu's low-level privilege level is
        set to privileged - this is done, implicitly, for
        each system call API - after this, appropriate
        system service routines of kernel components are
        executed - kernel components reside, in kernel
        space and execute, with higher low-level privilege -
        this gives them access to most resources, including
        IO - still there are restrictions,due to high-level
        privileges of the OS - this is based on policies,
        like normal user/root user/others

        - refer to the big picture diagrams

        - most of the above rules apply to hw interrupts and their
        processing - mode switching and higher low-level privileges
        are the same

        - so, if there is an application/non-core component executing,
        in user-space,
        we say, that a process is executing, in "user-space" - this
        is known as a "process context of execution"

        - in addition, if a non-core component/application invokes
        a system call API, some core services/components are
        invoked /processed, in the same process context - so,
        when a system call is executing, we still say, that
        a process/process context is executing
note: many principles of process context apply to thread context,
        as well
        - without a process (or a thread context), blocking
        , suspension, or other operations are disallowed -
        this is the design philosophy of Unix /Linux
note most of these principles apply to EOS/RTOS platforms, as well
        - even in the case of resources/managment, processes
        play main role - memory management is a topic, which
        is completely built around processes

        - in addition, if there are int. events, corresponding
        ISRs/handlers are processed, in "interrupt context"
        of execution, "not process context" of execution -
        there are several restrictions, for interrupt context
        of execution, in the system - typically, interrupt
        events / their processing deals, with time-management
        , scheduling, IO processing - eventually, after processing
note so, as in a typical embedded firmware, interrupt
        processing is highly restricted to critical
        jobs only and major jobs must be completed, in
        processes/process contexts ???
        after int. events, corresponding process/service will be resumed,
        unless there is a preemption / rescheduling - some of these
        points will be cleared, after understanding cpu scheduling,
        in operating systems ??

        - system call APIs generate system interrupts/traps and
        their behaviour is similar to hw interrupts, but the
        context of execution is process - in addition, system
        call APIs generate synchronous interrupt events -
        the behaviour of system call APIs is not the
        same as hw interrupts, due to their context of
        execution ???

        - whereas, hw ints. typically generate asynchronous
        interrupt events - asynchronous processing, whereas
        system call APIs are synchronous processing ???

note : can we say, in the context of conventional embedded
       sw, main()'s execution context is a synchronous
       context and interrupt processing/ISR processing
       will be asynchronous ???

note : in addition, in GPOS/RTOS platforms, ISRs/ interrupt
        processing will also invoke kernel components/
        methods/call backs

note: are there any restrictions, for ISR CODE, in
        conventional embedded sw models ?? what are
        the restrictions ??
        - should not spend much time, inside an ISR
        - code must be short and processing must be short

noteL in the case of OS platforms, similar approach is
      followed and in addition, there are few more rules
      to be followed, in the OS platforms

    - following are some of the typical examples, for processes
      used, in managing system processes/services :

        - shells/CLI utilities

        - basic system utilities//query the system /ps /top

        - system daemons/services, like
        init or systemd or cron/crond or
        sshd or any suitable system service/daemon

        - in typical Unix/Linux system, processes
        are created and managed, in a parent-child
        hierarchy. - this begins, with the first set of
        processes, including init or systemd

        - what is special about init or systemd ??
        - depending upon the Linux distribution and
        version, init or systemd will be the
        first user-space process/system process
        created, by the core of the operating system
        note: this is true, in embedded OS/RTOS , as well
        - as part of the booting/initialization of
        the core of the OS, several system processes
        are created, including kernel threads -
        kernel threads are light weight processes
        created, in system space and managed, in
        system-space, for core services

note : most of these apply to GPOS systems, but a simplified
        form of these apply to RTOS/EOS
        - in addition to these kernel threads, there
        are several user-space processes created,
        starting with init or systemd
note : in any OS, including GPOS or EOS or RTOS, a set-up is
        managed, using a set of processes or threads or hybrid

        - once systemd (System and Service Manager)is started, it will use
        a large set of configuration files of the
        OS to load/launch/create system services,
        as per the system's user-space configuration

        - typically, the process id of init/systemd is
        1 - so, it happens to be the parent of the
        entire hier. of user-space

        - in addition, once all the set-up is done,
        we can login and create sessions, which
        contain shells and terminals

        - using shells' CLI, we can run external
        and internal commands, for administrative
        or testing purposes

        - whenever we run/ load external commands
        on a shell , the shell acts as the
        parent process and generates children
        processes - this is based on the
        parent -child hier., as mentioned before

        - administrators also interact, with systemd
        , using systemctl (Systemctl is a systemd utility which is responsible for Controlling the systemd system and service manager.)to launch/testing services
        manually - in these cases, systemd is the
        parent process of the services/daemons
        started

        - in most cases, systemd can be automated to
        launch/load services, during boot-up time of
        the OS, but the basics remain the same

        - due to the parent-child hier. design principle,
        ideally, a parent process must clean-up a
        terminated children processes

        - however, if the parent process terminates, before
        the children processes, the orphaned children
te
        processes are reparented to the init or systemd
        of the system - so, the orphaned processes
        are assigned ppid 1 - similarly, daemon processes
        are also assigned ppid 1

        - a shell is a system utility, which is run, as
        process, for CLI - each shell instance uses
        a system terminal/interface for user interaction -
        - based on the shell/terminal set-up, there are
        following handles/descriptors - standard input
        descriptor, standard output descr., and std. error
        descriptor of the associated terminal - these
        handles/descriptors are maintained, as part
        of the shell process

        - so, the shell uses the above descriptors/handles
        to access the corresponding terminal - the same
        handles/descriptors are passed to external commands
        /utilities/and their respective processes - in the
        case of external commands, it is also maintained,
        as part of processes

        - in the context of Linux, bash shell is the
        commonly used default shell, but you may
        use other shell implementations, as per choice

        - a shell supports internal commands, which are
        interpreted and executed, by the shell program/
        process, without additional children processes

        - however, if external utilities/programs are
        executed, for each external utility or program,
        one or more children processes are created and
        launched

        - typically, when a command/utility is executed
        on the shell prompt, without &, a foreground
        process/job is created - this means, the current
        terminal is used, by the foreground process/job
        and the shell is not available, temporarily

        - the command/utility can take inputs, from the
        user , as well as ouput data to the terminal

        - in addition, certain hot-keys are applicable to
        the foreground job/process

        - interactive commands/utilities need to be
        executed, as foreground jobs/processes

        - on the other hand, if we execute a command
        or utility as a background job/process ,
        it does not use the terminal, for input,
        but can use it, for output - in addition,
        the shell can be available and interactive
        using the terminal

        - we can have several background jobs/processes
        executing, in a given shell

        - so, using foreground processes/jobs or
        background processes/jobs is more of
        practical convenience

        - from a typical OS perspective, these are
        just processes - however, from shell and
        terminal perspective, we have jobs -
        it is just the context and certain features

        - we can use jobs built-in command to
        list the shell's jobs

        - we can manage jobs/processes, using
        kill command, which is a built-in -
        it can take a job no or process no -
        still, it does the same operating, but
        the usage and perspective is different

        - one of the features of the shell is
        terminal redirection, where a descritor
        of a process is redirected to another
        sink or source, other than terminal

        - for instance,in the case of
        ls -li > ls.txt, following is done :

        - the standard output of the
        child process executing ls is
        being redirected to a file descriptor
        of ls.txt

        - so, effectively the output of ls will
        be pushed into ls.txt

        - for instance, what happens, in the case of
        ps -e -o pid,ppid,cmd,stat | less ??

        - ps is an external command, which is
        used to list the attributes of the
        current processes
        - less is another external command,
        which is used to take input and
        display one page, at a time
        - shell creates 2 children processes,
        for ps and less, respectively

        - so, one child process will load
        and execute ps and another will
        load and execute less

        - shell will also create an unnamed
        pipe, which will be used to
        interlink the processes - we say
        that pipe is an IPC object/entity/
        mechanism of OS services - in this case
        , shell uses this service,for its
        children

        - in addition, standard output of the
        process of ps is redirected to
        input descriptor of the pipe
        - same way,input descritor of
        less is redirected to output
        descriptor of the pipe

        - this effectively creates a link
        between the two child processes and
        effectively the utilities

        - in the above set-up, it is the shell
        that invokes appropriate system call
        APIs of the OS/kernel to facilitate
        the execution of commands and interlinking,
        as needed - shell is a classic example
        of a non-core component, but uses
        core services/system call APIs, for
        most of its responsibilities ??

        - let us use a few special commands,
        like sudo or su ??
        - for instance, let us deal, with
        su - root

        - what does su - root do ??
        - effectively, what does it do ??
        - when this command is executed,
        a new login shell/session is
        set-up, with uid/euid set to
        that of root - gid/egid is
        that of the current normal user

        - what does su - babu do ??
        - effectively, what does it do ??
        - when this command is typed
        , a new login bash/session
        is set-up, with the corresponding
        normal user's credentials, like
        uid/gid ?? also, euid and egid ??

        - based on the above set-up and details,
        what are we achieving, after
        su - root ??
        - this shell/process is privileged,
        as it is empowered, with uid /euid
        of root user

        - in addition, all children processes
        created from this shell will inherit the
        same uid/euid and privileges

        - so, we can access most OS services,
        using appropriate system call APIs
        - if we do a listing of su or sudo,
        we will see -rwsr-xr-x, which means,
        an extra attribute set-uid is set, in
        file's permissions - this extra attribute
        will change the uid/euid of the process,
        which executes su or sudo - from here on,
        su or sudo will be able to create
        powerful shells, as per the credentials
        of the target login user

i - similarly, sudo is another utility, which
        can be more controller, by the administrator
        and delegate limited powers to other normal
        users, whereas su is too powerful, for
        root user permissions

------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------
Process Multitasking

- let us take look at some of the big pictures -
  refer to the big-pictures and understand the
  set-up of processes - understand the user-space
  set-up of processes and understand the system-space
  set-up of processes

- as per operating system definition, each
  active application is managed, using a
  process
- as per operating system set-up,
  we can have several active processes,
  in the system, at the same time - this is
  the beginning of multitasking ???

- process is an operating system entity/service -
  we need operating system support, for processes
- without OS support, we cannot create/delete/
  manage processes

- every active application is managed using
  an unique process - most common case is
  one process for each active application -
  however, in the real-world implementations,
  there are other scenarios ??

- every process has a well defined set-up,
  in the operating system

- as part of the set-up, operating system/kernel
  maintain several system objects, for each
  process, in the system space - there is a
  a pd and a set of nested objects, for each
  process /active application - this is set-up,
  for every new process created, in the system
  - all these pds are managed by the system -
  in this case, process manager manages all
  the pds, in the system - this is the system-space
  perspective - the next provides the user-space
  perspective ??? pd contains enough information
  to manage and control a process - as we will
  see more, using the pd and its related information,
  we can control active applications/processes, during
  run-time

- user-space perspective of processes - in the
  user-space, a process is represented, using
  a process address-space - this address-space/
  memory map is not conventional, but uses
  logical or virtual addresses - so, the address-space
  /memory map is not of physical addresses,
  but logical or virtual addresses
note: in the case of conventional embedded
      systems/applications, we may use
      conventional address-spaces/memory-maps,
      based on the physical addresses
- for each process, there is a well defined
  address-space managed, for the process -
  this well defined address-space is exported
  to the user-space and used by the application
- in an OS platform, there will be several
  virtual/logical address-spaces, for
  several processes, in the system - meaning,
  there will one dedicated virtual/logical address-space
  per process
- in a conventional embedded platform, there will
  be a single address-space or memory-map
- so, the sw models used, in operating system
  platforms are more complicated, than sw models
  using, in OS-unaware platforms

- once you understand the basic set-up of processes,
  we use OS services to create and manage processes ??
- process creation, deletion and management is
  done, by process manager/subsystem of the
  OS/kernel
- process manager/subsystem is a core component of
  OS, so resides, in the kernel / kernel-space
note: in most text books/academic references,
      kernel is treated, as OS
note: use uname -r, for extracting version of
      core of the OS
note: use cat /etc/os-release, for extracting
      the complete OS version, which includes
      core + non-core components

- process manager exports appropriate system
  services, using system call APIs - these are
  known as process management system call APIs -
  some of the familiar APIs are fork() and execl()
- as a developer,the typical approach to
  accessing core OS services is to use
  system call APIS
- however, for convenience and operations,
  many of the OS services are provided, using
  system utilities - for typical system operations,
  system utilities are commonly used

- processes are typically used for multitasking,
  in larger applications - in addition, processes
  are used, in GPOS commonly - in addition,
  in specialized systems, where reliability and
  robustness is needed, processes are still used

- processes and threads may be used together, for
  multitasking, in real-world applications - initially,
  we will deal, with multitasking, using processes -
  later, with threads and hybrid models

- in an Unix/Linux system, processes are involved,
  in managing most services - many of the non-core
  services use processes,as the base, for
  multitasking

- every process is assigned its own process-address -
  this address space is set-up, using logical or
  virtual addresses of the processor and OS -
  in addition, each address space is mapped to
  corresponding physical addresses, using tables
  like page tables

- logical addresses/virtual addresses/address-spaces
  are provided, by processor and OS platforms -
  processor provides low-level features and
  it is the OS, that actually manages the
  address-spaces, for processes
- in typical embedded scenarios, we may
  come across following nodes :
     - sophisticated nodes, with processors
       supporting MMU(Memory Management Unit), virtual addresses/virtual
       address-spaces
     - sophisticated nodes, with processors
       supporting MPU(Memory Protection Unit), no logical/physical
       addresses
     - simple nodes, with processors
       , without MMU/MPU
- in all the above cases, we may OS platforms,
  for the systems
- in the case of GPOS, we will be dealing,
  with processors supporting MMU/virtual
  address-spaces/virtual addresses

note: we will see more details, during
      memory management of processes and
      system
- as part of the process address-space, a large
  portion is exported to user-space and the
  active application - refer to pdfs and diagrams

- currently, let us accept the basic set-up
  of processes and their address-spaces, and
  we will explore more, during memory management

note: many of the fields of pds of processes
      are used to manage the processes and
      most important of them is pid ?? we can
      treat this, as the handle to a process ??
- every process is managed using a pd/system
  object, which maintains attributes of a
  process, like :
        - pid - process identifier

        - user credentials of the sesssion

        - state of the process ??

        - scheduling parameters of the process

        - pointers to nested objects

        - these nested objects are used to maintain
        resources on-behalf of the process

        - maintain hw context on-behalf of the process

- pd of a process is used to manage and control the
  process - how is it possible to manage / control
  a process, using its pd ??

- based on the run-time state of the process, the
  pd of the process is maintained, in different
  lists/queues of the system, like rqs and wqs of
  the system ??

- using pid of the process and system utilities/
  system call APIs, we can control a process/
  active application, as needed ???

- let us understand processes, using certain
  scenarios /demos/commands ?? creation of
  processes and listing their attributes ??

- let us understand life-cycle of a process,
  using certain scenarios/demos/commands ???

- for instance, let us launch /load a set
  of applications/instances, as processes :

   taskset 0x00000001 ./w1&

   taskset 0x00000001 ./w1&

   taskset 0x00000002 ./w1&

   taskset 0x00000002 ./w1&

    ./w1&

    ./w1&

note1 : & is used at the end of the command to
        launch the application/program, as a
        background process, in a shell

note2 : if & is omitted, the command is
        launched , as a foreground application
        /program/process, in a shell

note3: taskset is used to launch /load an
        application/process and bind it to
        a specific processor - this mainly
        common, in the context of multiprocessor
        systems

note4: in this context, we are using taskset
       command, for binding/pinning a process
       to a specific processor, but in a
       real-world system, it may be achieved,
       using certain configuration file, but
       the basics remain the same and
       effectively binding/pinning is achieved

- after loading/launching the above demos,
  let us monitor the status of the processes,
  using ps and top commands ??

    - ps is a static utility, which just captures
      the current state of processes and lists
      the details

    - whereas, top will periodically update the
      details of processes, dynamically

    - as per convenience, we can use ps and top,
      accordingly

    - follow the demos and the commands/options

- what happens, when one or more processes/commands/
  applications are launched, in a session/shell of
  a root user ??
      - in this context, shell has the user-id/
        credentials of root user - these are passed to the
        children processes

- the above credentials will be used/discussed,
  during access model of the OS ??

- let us understand states and state diagram of
  processes :

    - following are the typical states of
      a process:
        - ready state, in an rq of scheduler
        of a cpu/processor

        - running / on the cpu - scheduled/
        dispatched

        - blocked state - waiting/sleeping
        for resources/events

        - suspended state/stoppped state -
        in this state, the process is
        explicitly suspended, by the
        developer/administrator/core of the
        system

        - terminated state - the process is
        terminated - resources are freed -
        eventually, the process is deleted

- let us understand a typical life-cycle of
  a process :

    - a typical process is created, using
      one or more system call APIs, directly or
      indirectly

    - once process is created, its pd is added
      to an Rq of the scheduler - currently, let
      us assume, that we are dealing,with
      uniprocessor system - later, we can expand
      this to multi-processor systems

    - all ready processes/pds are maintained, in the
      Rq of the scheduler of the system

    - typically, OS scheduler will be invoked
      , as per the rules of the system and it
      will select the most eligible process/pd
      from the Rq and dispatch it to the
      processor

    - once dispatched, the process/pd will be
      executed on the processor, for certain
      time-quantum, as per the scheduling
      policies and paramters - let us assume, that
      the current policy is time-slicing and round-robin

    - based on the above scheduling policy and
      time-quantum, every process/pd will be
      scheduled/dispatched, as per their merit -
      in addition, once scheduled/dispatched,
      a process will be preempted, after a time-
      quantum/time-slice and this will be repeated,
      forever !!!

     - in this set-up, hw timer/timer int. events-->
       hw timer ISR ---> scheduler --> preemption -->
       rescheduling --> this is repeated, every
       time-quantum ???

     - as part of the above actions, preemption of
       a currently executing process is done, which
       will forcibly remove the process/pd from the
       cpu and move to Rq - meaning, from
       running state to ready state

     - typically, when a process/application is
       scheduled and dispatched,it may invoke
       one or more system call APIs, for accessing
       resources - however, if the resources are
       currently unavailable, the process is blocked,
       in an appropriate wq - we say, that the
       process is blocked/sleeping/waiting and
       the state of the process is blocked/sleeping ??

     - typical scenarios can be network IO, disk IO,
       interprocess communication channels, like
       sockets are possible cases, for blocking/sleeping

     - typically, starting a service/server service
       will require certain system utilities, but the
       above basics of process creation/mangement
       remain the same

     - similarly, we may stop or terminate a service,
       which will lead to actual termination of the
       process/active service - typically, this is done,
       for maintenance reasons only ???

     - when a process is terminated, its resources are
       freed and typically deleted - however, the actual
       implementation of process termination varies,
       from one system to another - for example, in the
       case of Linux/Unix, there is an intermediate
       termination state known,as zombie and a final
       termination state, known as DEAD

     - there are different forms of termination -
       normal termination and abnormal termination -
       abnormal is forced termination - so, depending
       upon the requirements, the applications / services
       are normally or abnormally terminated

     - when a process is blocked/sleeping, for
       resources / IO, it will be unblocked /
       awakened, once the resource/IO is available
       and added to the Rq - once added to the Rq,
       the process will be scheduled/dispatched,
       as per their merit of scheduling policies
       and parameters

     - typically, suspended/stopped state is an
       explicit state, for the processes, which
       can be achieved, by the developer/administrator/
       system to suspend/stop a process, forcibly
       - we can explicitly resume the process
       , using system utilities, if needed - suspending
      a process is not same,as that of terminating
      a process - it is a temporary state, for
      process control

 - since there are several resources/IO channels/
   IPC channels, in the system, there will be several
   wait-queues/wait-lists, in the system, where a
   process/pd will be added and blocked

 - if a process/active application is terminated
   normally or abormally/forcibly, the process
   will be moved to Zombie and later, it will
   cleaned-up, by the parent process - once
   cleaned-up, the Zombie process will be
   moved to DEAD state - the pd of the process
   is completely deleted, from all the lists
   of the system - there will be no traces
   of the cleaned-up process, in the system -
   you will never be able to monitor it, using
   any tool

- let us understand process scheduler/cpu scheduler
  of OS :

   - process scheduler/cpu scheduler is invoked
     by the system, due to interrupt events,
     system call events and other events

   - in the above case, scheduler invokation,
     due to interrupt events are typically
     preemption points

   - on the other hand, scheduler can also be
     invoked, due to other events, like blocking
    and termination of processes

   - cpu scheduler is a component of core of
     OS - a core component - it has two
     sub-components - one is the scheduler or
     selection of the next process/pd, as per
     the scheduling parameters/policy

   - the other component is the low-level
     dispatching component, which is responsible
     , for dispatching a process/pd to a processor,
    using the hw context of the process/pd - such
    low-level details are common, in the context
    of OS

   - in our further discussions, we will understand
     certain practical scheduling policies and
     their behaviour - in addition, we will understand
     , how they can influence the scheduling
     and execution of processes/applications/
     services

   - initially, let us understand uniprocessor
     scheduling, but later extend the details
     to multiprocessor scheduling

   - signals/notifications

      - it is an IPC mechanism, which is used to generate
        notification to process/processes

      - in a typical Unix/Linux system, several signals
        are supported - as many as 64 signals/notifications
        are supported

      - many of the signals/notifications have a predefined
        role, by the GPOS

      - meaning, these are generated, for specific events
        and purposes

      - these notifications can be generated, explicitly or
        by the system - meaning, we can generate a signal
        /notification to a target process, using a system
        call API or system utility

      - in addition, system will generate several notifications,
        for extreme events, like fatal exceptions and low
        memory scenarios

      - every process/pd maintains a signal pending field, where
        each bit represents a signal/notification - so, if a
        signal is generated, for this process/pd,corresponding
        bit is set - we say, that a signal is generated

      - before we understand more details on signal generation
        and handling/processing, let us understand certain
        use cases of signals
        - to forcibly/abnormally terminate a target process,
        we use SIGKILL signal
        --> kill -SIGKILL <pid> //send a signal to
        //a specific process

        --> killall -SIGKILL <nameofapplication>
        //send a signal to
        //every process managing
        //active instances
        //of an appplication/
        //program

        -->kill -SIGSTOP <pid>

        //forcibly stop a process, for
        //administrative reasons

        -->kill -SIGCONT <pid>
        //resume a process, for
        //admin. reasons

        --> ctrl-C will generate
        SIGINT to foreground processes/process
        - by default, the foreground process/
        processes are abnormally terminated

        --> ctrl-Z will generate SIGTSTP to foreground
        processes/process - the current foreground
        process will be stopped

        --> SIGSEGV will be generated,when a process
        encounters a fatal exception, due to
        illegal memory access ??? the process or
        application will be forcibly
        terminated - it is a form of crash -
        in this case, system generates SIGSEGV
        to the process/application

        --> when the system runs into low-memory
        scenarios, in a virtual memory management
        system,system will generate SIGKILL to
        processes to reclaim the memory resources
        - this is one of the possible scenarios,
        where system again generates the signal to
        target processes

        --> for instance, SIGHUP/hang-up signal is
        generated for target processes of
        services to force a reload of their
        configuration files, during run-time
        - this true, for most services/daemons
        , in an Unix/Linux system

        --> for instance, if a typical service/daemon
        is managed, using systemd
        - let us assume the service/daemon is
        started/launched during boot-time or
        run-time - in addition,if we wish to
        change its run-time configuration, we
        can do it, by generating a SIGHUP signal,
        using systemctl utility

        --> during the run-time, if the configuration
        file is changed, using systemctl command
        we can force a SIGHUP to the target process/
        service/daemon, using appropriate options ???

        --> in this case, which process is the target
        process ?? the target process will be
        the service/process which needs to
        reload its configuration file ???
        - it can be any service, like
        nginx, sshd, or cron/crond, and
        many more ??

        --> in this case, which entity/process/core
        component is generating
        the signal/notification ??
        - in this case, systemctl generates
        a message to systemd, using
        its own IPC mechanism, like sockets

        - systemd will generate appropriate
        notification to the target
        process/service

        --> in this case,what is the action/handling
        taken, for the notification of the signal
        ???
        - in this case, the action taken
        is re-reading the configuration file
        and changing the operations, accordingly

        - so, following is the typical summary for
        signal management, in a Unix/Linux systems :
        - signals/notifications are generated,
        by processes/utilities(including shell)
        or system/core
        - when a signal is generated/notified to
        a target process, corresponding signal
        is recorded/generated, in the pd
        - once recorded, certain action/actions
        is taken, as per the settings, for
        the signal
        - in most cases, default settings and actions
        are used
        - in certain cases, instead of default settings
        and actions, a customized action can be
        set-up, for the process/application/daemon

        - in the case of SIGKILL, only default action
        is allowed , so the system will abnormally
        /forcibly terminate the target process

        - in the case of SIGSTOP or similar SIGTSTP,
        the default action will be to forcibly
        stop/suspend the process/service

        - in the case of SIGSEGV, system generates the
        signal to the process and process is abnormally
        /forcibly terminated

        - in the case of SIGHUP, instead of default action,
        there will be a custom action, where the
        target daemon /service will re-read the new
        configuration file and take actions